## Slide 1: Networks
Malone, Thomas. 15.561 Information Technology Essentials, Spring 2005. (MIT OpenCourseWare: Massachusetts Institute of Technology), http://ocw.mit.edu/courses/sloan-school-of-management/15-561-information-technology-essentials-spring-2005 (Accessed 19 Nov, 2014). License: Creative Commons BY-NC-SA

## Slide 2: Outline
Point to point connections
  Representing information
    Analog vs. digital
    Representing words and picture
  Communications media and bandwidth
Networks
  LANs vs WANs
  Circuit switched vs. packet switched
Example: The Internet
Network protocols
  Enterprise networking
Example: Looking at a web page
Wireless networks
  Wireless telephony
  Wireless data communication

## Slide 3: A simple point-to-point connection
Process convert data into signals
Signals are transported through channels
Channels utilize one or more connection media

## Slide 4: Data: Analog vs. Digital
Analog data
  Can take on any value within a continuous range
  Examples:
    Human voice
    Boston’s temperature
Digital data
  Can take on only a finite set of discrete values
  Examples:
    Data stored in binary computers
    The US standard size of clothes

## Slide 5: Representing Numbers
Number | 4-bit binary representation
1 | 0001
2 | 0010
3 | 0011
… | …

## Slide 6: Representing Characters
Character | ASCII* Representation
A | 1010 0001
B | 1010 0010
C | 1010 0011
… | …
0 | 0101 0000
1 | 0101 0001
… | …

## Slide 7: Formatted Documents
In addition to text, must contain information about how it appears on paper
  Bold, italic, underlined text
  Different sizes of type
  Page breaks
“Invisible” formatting characters are embedded in text
  Special “begin formatting” character
  Format specification character (i.e. “bold type”)
  Text string for which formatting applies
  Special “end formatting” character
Same character codes have different meaning when interpreted as letters and when as format specifications
  65 could mean either ‘A’ or ‘bold’ depending on context

## Slide 8: Formatted Documents (cont’d)
Example:
  This is nicely formatted line.
Could be stored internally as:
  <BG PAR> ‘T’ ‘h’ ‘I’ ‘s’ ‘ ‘ ‘I’ ‘s’ ‘ ‘ ‘a’ <BG UNDERLINE> ‘n’ ‘I’ ‘c’ ‘e’ ‘l’ ‘y’ ‘ ‘ <EN UNDERLINE> <BG COLOR>1 ‘f’ ‘o’ ‘r’ ‘m’ ‘a’ ‘t’ ‘t’ ‘e’ ‘d’ <EN COLOR> ‘l’ ‘I’ ‘n’ ‘e’ ‘.’ <CR>
Where:

## Slide 11: A Simplified Computer
Numbers, letters, and words are not enough: we want pictures
Representing a picture
  Draw a very fine grid on it
    Grid cells are called pixels or dots
  See what is in each grid cell
    Bitmap: is cell empty or full?
    Grayscale: how dark is the cell?
    Color: what color is the cell?
  Represent each cell with a pre-specified # of bits (how many?)
  Store the bits for the cells in a pre-specified order
    e.g. all the cells for the top row, then the next row, etc.

## Slide 13: Digital Convergence

## Slide 14: Connection media – Examples
Medium Speed Cost
Twisted wire 30 BPS – 10 MBPS Low
Microwave 256 KBPS – 100 MBPS
Coaxial cable 56 KBPS – 200 MBPS
Optical fiber 500 KBPS – 10 GBPS High
BPS = bits per second

## Slide 15: What is bandwidth
Technically:
  The range of usable frequencies in a communications medium
Practically:
  The amount of information that can be carried by a communications medium per unit of time

## Slide 16: Multiplexing: Squeezing many channels into one
Frequency Division Multiplexing (FDM)
Time Division Multiplexing (TDM)

## Slide 17: Why build networks?
Full Connectivity doesn’t scale!

## Slide 18: Networks are about sharing
The network allows an entity to switch its attention among a large number of others
Permits sharing of resources attached to the network, including the resources of the network itself

## Slide 19: Local and Wide Area Networks
Local Area Networks (LANs)
  Short distances
  Within organizations
  Typical technology: Ethernet or Token Ring
Wide Area Networks (WANs)
  Long distances
  Across organizations (typically multiple LANs)
  Typical technology: Public Switched, Leased Line

## Slide 20: Two forms of network connection
Circuit switching
  A dedicated end-to-end connection is established for the duration of the connection
  Used in telephone network
Packet switching
  Messages are divided into small packets
  Each packet is separately routed to the destination
  Different packets can take different paths and times
  Missing or garbled packets are retransmitted, if necessary
  Packets are reassembled into messages at the destination

## Slide 21: Packet switching

## Slide 22: Packet switching
Circuit switching | Packet switching
Minimum delay | Variable delay
Very inefficient use of connection capacity | Much more efficient use of connection capacity
When overloaded, unable to make connection at all | Can almost always connect, but may be long delays
Both ends of connection must use same data rate | Data-rate conversion is easy

## Slide 23: The Internet
What is the Internet?
  Outgrowth of ARPANET
  Based on TCP/IP
  A collection of interconnected networks
  Provides appearance of widespread connectivity
What is it used for?
  E-mail, file transfer, terminal access, client-server traffic, information browsing (aka Web), distributed work, electronic commerce, etc.

## Slide 25: Internet Address (IP address)

## Slide 26: Understanding Internet Addresses
18.154.0.27
  Uniquely assigned to a specific Internet connection point
  32-bit address
  Each number between dots is the decimal representation of 8 bits in the address
  In this case:
    18 specifies MIT (MIT owns all addresses 18.xxx.yyy.zzz)
    154 specifies the subnet corresponding to building E56
    0.27 is host number within the subnet
  Every internet address can optionally have a descriptive host name (e.g. LASAGNA.MIT.EDU)

## Slide 27: Who controls the Internet?

## Slide 28: What does it mean to be on the Internet?
Run TCP/IP protocol
Have an IP address
Have ability to send IP packets to other machines on the Internet

## Slide 29: Network Protocols
Rules of behavior
  What, when, and how should A send messages to B and vice versa?
Protocol layers
  Each layer uses the layers below it and can be used by the layers above it
  Often, multiple alternatives can be substituted at one layer without affecting the other layers

## Slide 30
Example: TCP/IP protocol architecture
Application layer Provides communication between applications on separate machines (e.g. email, file transfer, web browsing)
Transport layer Provides end-to-end reliable data transfer across multiple networks (e.g. TCP – Transmission Control Protocol)
Internet layer Routes data from source to destination through one or more networks (IP – Internet Protocol)
Network access layer Manages logical interface between a machine and its local network (e.g. Ethernet, X.25)
Physical Layer Converts bits to signals and back (e.g. wires, radio, etc.)

## Slide 31: Different types of connection protocols
X.25 – A packet switching protocol for connecting devices on a WAN
Frame relay – Another packet switching protocol for connecting devices on a WAN (faster but less error checking than X.25. Up to about 45 Mbps)
Asynchronous Transfer Mode (ATM) – A “cell switching” protocol that establishes “virtual circuits” from fixed size packet (faster than X.25, e.g. suitable for real-time video. Up to about 622 Mbps)

## Slide 32: Different types of connection “boxes”
Hub – Connects parts of a network, typically different parts of the same LAN (network access level)
Bridge – Connects two LANs using software (network access level)
Switch – Connects different LANs, typically using hardware only (network access level)
Router – Connects two networks that may or may not be similar and routes packets appropriately (Internet level)
Gateway – Connects networks that use different protocols (transport level or above)

## Slide 33: Example: The World Wide Web
A collection of interlinked documents stored on computer servers all over the world and accessible to user clients via the Internet
  Documents communicated in HTML (Hyper Text Markup Language)
  Rules for requesting and providing documents (and other interactions between clients and servers) are defined by HTTP (Hyper Text Transfer Protocol)
Documents may contain easily “clickable” links to other documents.
  Documents are identified by “web addresses” called URLs (Uniform Resource Locators)
“Hypertext” means text documents that contain embedded links to other documents.

## Slide 34: Looking at a Web page
Connect your PC to the Internet
  Dialup an Internet service provider (via modem)
  Establish a point-to-point link with the provider’s machine
    Using PPP (Point-to-Point Protocol)
    Your PC receives a “temporary IP address)
      Using DHCP (Dynamic Host Configuration Protocol)
    Your PC receives the address of a Domain Name Server (DNS)
Start your browser program (e.g. Internet Explorer)
Type in a URL (Uniform Resource Locator)

## Slide 35: Looking at a Web page (cont.)
Brower asks DNS for the IP address of the MIT Server
DNS replies with 18.170.0.167
Browser opens TCP connection to 18.170.0.167
Browser sends the command GET/class/syllabus.htm
The MIT Server sends file syllabus.htm
TCP connection is released
Browser displays the contents of syllabus.htm

## Slide 36: How a cell phone works

## Slide 37: Cellular Phone Networks
Frequency reuse
Handoff

## Slide 38: Cellular Phone Networks
Frequency reuse
Handoff

## Slide 39: Cellular Phone Networks
Frequency reuse
Handoff

## Slide 40: Cellular Phone Networks
Frequency Multiple Division Access (FDMA)
Time Division Multiple Access (TDMA)
Code Division Multiple Access (CDMA)

## Slide 41: Generations of cellular technology
First Generation (“1G”, 1980’s and 90’s)
  Analog, primarily used for voice, low bandwidth (e.g. 9.6Kbps)
  Ex: AMPS (USA)
Second Generation (“2G”, 1990’s and early 2000’s)
  Digital, cheaper, somewhat higher bandwidth (e.g. 14.4 Kbps), more data services (e.g. short messages, caller ID)
  EX: GSM, TDMA, CDMA, PCS
Third Generation (“3G”, started 2002)
  Digital, much higher bandwidth (e.g. 2Mbps), many more services (e.g. video)
  Ex: WCDMA, CDMA2000

## Slide 42: Different cellular standards
Standard | Appx. Freq. (MHz) | Mode | Multi-plexing method | Voice/ radio Channels | comments
Analog (AMPS) | 800 - 900 | Analog | FDMA | 1 | Common in US, but becoming obsolete
GSM | 900, 1800 - 2100 | Digital | TDMA | 8 | Common in Europe & Asia, growing in US
CDMA (IS-95) | 800 | Digital | CDMA | 20 – 60 | Qualcomm holds key patents
TDMA (IS-54 & IS 136) | 800, 1800 – 2000 | Digital | TDMA | 3 – 6 | Most common “digital” cellular in US
PCS | 1800 – 2100 | Digital | - | - | Generic term for 1800 – 2000 MHz svcs
WCDMA | Many | Digital | CDMA | Many | Migration path from GSM. Up to 2 Mbps.
CDMA2000 | Any | Digital | CDMA | Many | Migration path from CDMA. Common in S Korea. Up to 2 Mbps

## Slide 43: Cellular acronyms
AMPS – Advance Mobile Phone System
CDMA – Code Division Multiple Access
FDMA – Frequency Division Multiple Access
GSM – Global System for Mobile Communication
IS – Interim Standard
PCS – Personal Communications Services
TDMA – Time Division Multiple Access
WCDMA – Wideband CDMA

## Slide 44: What is Wireless IP?
A wireless connectivity solution employing IP that enables devices to access an Intranet or the Internet
PDAs
Cellphones
Pagers
Laptops
Workstations
Future Devices?

## Slide 45: Wi-Fi (Wireless Fidelity)
Protocol for wireless LANs
802.11b format – 11Mbs
802.11g format – 20+ Mbps
Allows you to
  Connect to Internet in local “hot spots”
  Connect many PC’s to the Internet through one access point

## Slide 46: Bluetooth
Wireless device connectivity
Named after Scandinavian king who united several unruly kingdoms
Short range (<10m)
Sample uses
  Wireless PDAs always connected to desktop via mobile phone
  Wireless headphones connected to notebook
  Office / Home device networks that automatically reconfigure by presence
  …

## Slide 47: How will networks change business?