## Slide 1: Information Technology Essentials
Technology
Applications of Technology
Malone, Thomas. 15.561 Information Technology Essentials, Spring 2005. (MIT OpenCourseWare: Massachusetts Institute of Technology), http://ocw.mit.edu/courses/sloan-school-of-management/15-561-information-technology-essentials-spring-2005 (Accessed 19 Nov, 2014). License: Creative Commons BY-NC-SA

## Slide 2: Why bother?
Why should you, as a manager, care about information technology?
Notes: This is the only time the class will go at this nice pace.

## Slide 3: Main Course Objectives
Become comfortable with the technologies that are shaping business today
Acquire tolls that will help you assess technological trends long after you have left Sloan

## Slide 4: A Typical Computer

## Slide 5: A Simplified Computer

## Slide 6: A Simplified Computer
Memory
There are 100 “locations” on the blackboard
Each location has room for one 3-digit number
Load moves number from blackboard to register. Example: LOAD 01
Store moves number from register to blackboard. Example: Store 00

## Slide 7: A Simplified Computer
Input/Output
Input and Output conveyors hold 3-digit numbers.
GET moves number from input to register.
Put moves number from register to output

## Slide 8: A Simplified Computer
Processor/Calculator
Register has room for one 3-digit number.
Calculator can add and subtract numbers from memory to register.
Example: ADD 02
SUBTRACT 03

## Slide 9: LMC INSTRUCTIONS
Get
Put
Load x (Load 01)
Store x (Store 05)
Add x (Add 02)
Sub x (Sub 03)
Stop

## Slide 10: SYMBOLIC LMC INSTRUCTIONS
Example Instruction Sequence
Calculate Pay = Wage + Bonus
Load Wage
Add Bonus
Store Pay
Stop

## Slide 11
STEP INSTRUCTION STEP INSTRUCTION
1. 5.
2. 6.
3. 7.
4. 8.
Program to:
Read WAGE and BONUS amount from INPUT
Compute total PAY
Output total PAY

## Slide 12: LMC STORED PROGRAM CONCEPTS
ISSUES:
Where is LMC program stored?
How does LMC understand instructions like STOP? It only likes numbers.
How does LMC handle symbolic labels like A, B, C
ANSWERS (Stored Program Concept):

## Slide 13: LMC MACHINGE LANGUAGE AND ASSEMBLY LANGUAGE

## Slide 14: INSTRUCTION SEQUENCE

## Slide 15: INSTRUCTION SEQUENCE
Control Flow
BRANCH always puts a new address in the instruction counter.
BRANCH ZERO puts a new address in the instruction counter if the REGISTER is 0. Otherwise it increases the instruction counter by 1.
Examples: BRANCH 02
BRANCH ZERO 06

## Slide 16: INSTRUCTION SEQUENCE
So what are:
MIPS and MHz all about?

## Slide 17: The Little Man Computer

## Slide 18: BASIC FACTS TO ASK ABOUT ANY COMPUTER
MEMORY
  BASIC UNIT 3 DECIMAL DIGIT NUMBER
  MAXIMUM SIZE 100 LOCATIONS
REGISTERS
  HOW MANY 1
  NUMBERS 3 DECIMAL DIGIT NUMBER
INSTRUCTIONS
  NUMBER 7 INSTRUCTIONS

## Slide 19: The ‘Real’ Computer

## Slide 20: INTEL PENTIUM 4 ANSWERS
MEMORY
  BASIC UNIT 8 BINATY DIGITS (BITS) = 1 BYTE
  MAXIMUM SIZE 32 BITS = 4 BYTES
  TYPICAL SIZE MEMORY RAM: 128 MB – 1GB
REGISTERS
  HOW MANY ABOUT 50 REGISTERS
  NUMBERS BARIOUS TYPES
INSTRUCTIONS
  NUMBER ABOUT 500
0 0 1 0 1 1 0 1
8 BITS

## Slide 21: Binary Computers
Real computers don’t store and calculate with 3-digit decimal numbers
A bit (binary digit) distinguishes between tow states
  TRUE and FALSE
  1 and 0
Bits are easier to implement in machines
  Light bulbs on or off
  High vs. low voltages (on wires)
  Magnetized or not (computer hard disks, floppies, tapes)
  Pit or no pit detected by a laser (compact discs)

## Slide 22: Interpretation of a decimal number
3 7 9
3x100 + 7x10 + 9x1
3x102 + 7x101 + 9x100

## Slide 23: Interpretation of a decimal number
1 1 0 1 1
1x24 + 1x23 + 0x22 + 1x21 + 1x20
1x16 + 1x8 + 0x4 + 1x2 + 1x12
127

## Slide 24: The CPU
CPU = Central Processing Unit
Internal clock ticks very fast (e.g. 1.6GHz = 1.6 billion ticks per second)
  Activities are synchronized to start on a clock tick
  Some activities take more than one clock tick
Instruction execution is automatic
  (tick) find memory address of nest instruction
  (tick) retrieve instruction from memory
  (tick) decode the instruction
  (tick) fetch argument from memory if necessary
  (tick) execution instruction
  (tick) store result in memory if necessary

## Slide 25: CPU and Memory Interaction

## Slide 26: CPU and Memory Interaction
CPU: I need the contents of memory location 50!

## Slide 27: CPU and Memory Interaction
Memory: Location 50 contains the number 127

## Slide 28: CPU Characteristics
Family: Determines the set of instructions it understands
  Intel 80386, 80486, Pentium, Pentium II, …
  Motorola: 68030, 68040
Clock Speed
  Pentium: 500 MHz – 2.2 GHz
Data bus width: Size of data that can be manipulated at one time
  80486: 32 bits, Pentium: 64 bits
Address bus width: Limits the amount of memory that can be installed in the computer
  LMC: 3 decimal digits. Location______
  Pentium: 32 bits. Location______
  Itanium: 64 bits. Location______

## Slide 29: Expressing Memory Capacity
Measured in bytes (=groups of 8 bits)
Each byte can store a binary number from 00000000 to 11111111 (255 = 28-1)
More generally: n binary digits can store numbers from – to 2n-1
Frequently used multiples:
  Kilobyte (KB) = 1,024 (210) bytes
  Megabyte (MB) = 1024 KB = 1,048,576 (220) bytes
  Gigabyte (GB) = 1,024 MB ~ 1 billion (230) bytes

## Slide 30: Semiconductor Memory
RAM (Random Access Memory)
  Can access any location equally fast
  Loses contents without power
  Two main types
    Static (SRAM): Faster, expensive
    Dynamic (DRAM): Slower, cheaper, consumes less power and space
ROM (Read Only Memory)
  Retains memory even without power
  Useful to store programs executed upon system start-up (e.g BIOS)

## Slide 31: Hard Disks and Floppies
Slower than main memory
Bits stored as magnetic field of different polarity
Magnetized surface of disk rotates under magnetized head (read/write mechanism)
Disk divided into tracks, each at different radius from center
Tracks are divided into sectors

## Slide 32: Hard Disk Geometry
Head moves back and forth
To read/write some data:
Head moves over desired track
System waits until desired sector passes under head
Data is read/written

## Slide 33: CD-ROMs
Slower than hard disks
Data is encoded by burning miniature “pits” on a photoreflective surface; read by laser
CDs can hold up to 650MB of data
CD-ROM drive maximum transfer speed is expressed in multiples of 150KB/sec
  4X drive  600KB/sec
  20X drive  3000KB/sec

## Slide 34: DVD (Digital Video Disk)
New, improved CD-ROM
  Smaller, denser, “pits”
  Two layers of “pits” recorded on the same disk
DVDs can hold up to 17GB of data

## Slide 35: Keychain drives
Hold 16MB – 2GB
Attach to USB (Universal Serial Bus) port
Usually use “flash memory”
  A special kind of ROM that can be rapidly erased and re-recorded

## Slide 36: I/O Devices
Input
  Keyboard
  Mouse
  Hard Disk
  Floppy Disk
  …
Output
  Printer
  Screen
  Speakers
  …

## Slide 37: Computer Displays
Computer screen divided into small dots (pixels)
Each pixel can be displayed in a different color
Screen resolution: Number of pixels per screen
  640 x 480
  1024 x 768
Color information for each pixel stored in memory, read and converted to video signal 60 times per second
  To store information for a 1024 x 768 screen with 256 possible colors for each pixel we need ______ bytes

## Slide 38: Buses: Connecting I/O to CPU
One set of wires connect all devices and CPU
  Transport of information is shared (public)
Nearly all computers use a bus to connect CPU and I/O Devices
Buses allow easy addition/replacement of I/O Devices
  Modern PCs come equipped with expansions slots, directly connected to the bus
  I/O Device controllers implemented as expansion cards
  Examples: ISA, PCI PCMCIA, IEEE 1394 (FireWire)

## Slide 39: A simple bus architecture

## Slide 40: Cache Memory: Motivation
Cheap main memory is slower than CPU
  Example: Pentium PCs
    CPU 2ns (500MHz)
    Main memory (100MHz SDRAM) 10ns
  Instructions that access main memory take many more clock ticks than those that don’t
Solution:
  Automatically keeps copies of most frequently used memory locations in fast (but expensive) memory = cache memory

## Slide 41: A modern PC architecture (simplified)

## Slide 42: Summary: A modern PC
Processor: Pentium (500 MHz - GHz)
Main Memory: 64 MB – 4GB
Floppy Drive: 1.44 MB (3.5-inch disks)
Hard Drive 10 – 500 GB
Graphics: 640 x 480 – 2048 – 1536, 256 to 16 million colors
Video Memory: 32 – 256 MB

## Slide 43: Types of software
System Software
  Operating systems
  Programming languages
  Database systems
Application Software
  General office tasks (word processing, etc.)
  Accounting
  Design
  Factory automation
  …

## Slide 44: Operating systems - Examples
DOS
Windows (95, 98, NT, 2000, XP)
Mac OS X
Unix
  Linux
…

## Slide 45: Operating system
Allocates and assigns:
  Memory
    e.g. file system, virtual memory
  Processor time
    e.g. multitasking, multiprocessing
  I/O devices
    e.g. printer, keyboard, etc.
May also provide other capabilities useful to many users or programs
  Graphical User Interface (GUI) capabilities
  Fonts, network protocols, …
  Web browser?

## Slide 46: Illusion #1: Multitasking
Reality:
  One CPU
  One instruction at a time
Illusion:
  Several application programs executing concurrently
Implementation:
  Operating system divides CPU time among application programs (time sharing)
    Each program “thinks” it is the only one running
    OS copies Instruction Pointer and Registers back and forth as each program takes its turn

## Slide 47: Multitasking issues
How is control passed to next task?
  Cooperative multitasking (Windows, Windows 95)
    Application explicitly passes control back to OS
    What if application never passes control back?
  Preemptive multitasking (Unix, NT, XP)
Can one task access the memory of another one?
  Preventing this is called “memory management”
  Done by Unix, NT, XP< Mac OS X (Not by older versions of Mac OS and Windows)

## Slide 48: Illusion #2: Virtual Memory
Some data is not used for a long time
  Why keep it all in memory?
Copy a unit of data (called a “page”) to hard disk and use memory for other data
Copy pages back from hard disk to main memory as they’re needed
Process (and its programmer) not aware that main memory is too small (the big memory illusion)
  It asks for a main memory location (Page #, offset on page)
  OS has to get that page into main memory if not already there

## Slide 49: Illusion #3: File Systems
Reality:
  Disks are set of tracks
  Tracks are sets of sectors
  Sectors can store fixed-sized byte blocks
Illusion:
  Disks are sets of directories
  Directories contain other directories or files
  Files are variable-size byte sequences
  Directories and files have names

## Slide 50: Illusion #4: Windows and Menus
Reality: Screen is an array of pixels
Illusion 1: Menus
  Depending on where you click, different action happens
  Technique: OS look up location where mouse was clicked, executes appropriate action
Illusion 2: Overlapping windows
  A window may cover part of all of another
  When a window is uncovered, its contents are redisplayed
  Technique: OS saves bitmap of covered windows
    Application does not need to know how to redraw the contents of its window

## Slide 51: Microcomputer Operating Systems
DOS
  Text-based interface, no multitasking
Windows
  Windows, cooperative multitasking
  Filenames restricted to 8 characters
  Bad memory management!
Windows 98
  Large filenames
  Built-in networking capabilities
  Plug-and-play device configuration

## Slide 52: Microcomputer Operating Systems
Windows NT (including Windows 2000, Windows XP)
  Full multitasking
  Full memory management
UNIX (including Linux)
  Great memory management, multitasking
  Complex, text-based interface
Mac OS X
  Based on Unix
  Easy to use
  Can only run on Macintoshes

## Slide 53: Selecting an Operating System
Is our existing software compatible with the OS?
Does the OS have a large base of compatible software?
How reliable is the OS? Does it crash frequently?
Is the OS available for a wide variety of hardware?
How quickly does it run?
How easy it is to learn and use?
How easy is it to install and configure?
How much does it cost?